## Slide 1: Problem Decomposition and Multi-shot ASP Solving for Job-shop Scheduling
Mohammed M. S. El-Kholany, MSc.
Supervisors:
Prof. Dr. Martin Gebser
Assoc. Prof. Dr. Konstantin Schekotihin
Production Systems Research Group
Department of Artificial Intelligence and Cybersecurity
Alpen-Adria-Universität Klagenfurt, Austria
ICLP 2022

## Slide 2: Agenda
Introduction
State of the Art
Methods
  Decomposition Strategies
  Overlapping
  Compression
Results
Conclusions

## Slide 3: Production Systems
Customized products and delivery deadlines make efficient production management highly complex
Challenges related to machines and resources' availability are raised
Production
Limited Resources
High Demands
Scarcity Problem

## Slide 4: Job-shop Scheduling Problem (JSP)
4 jobs with 3 operations and 3 machines
Processing time |  |  | 
 | Operation |  | 
 | 1 | 2 | 3
Job 1 | 4 | 3 | 2
Job 2 | 1 | 4 | 4
Job 3 | 3 | 2 | 3
Job 4 | 3 | 3 | 1
Machine assignment |  |  | 
 | Operation |  | 
 | 1 | 2 | 3
Job 1 | 1 | 2 | 3
Job 2 | 2 | 1 | 3
Job 3 | 3 | 2 | 1
Job 4 | 2 | 3 | 1
O 3,1
O 4,3
O 2,1
O 2,2
Machine 3
Machine 2
14
Machine 1
O 4,1
O 4,2
O 3,2
O 1,1
O 1,2
O 3,3
O 2,3
O 1,3
The time needed to complete all jobs “makespan”  14
12
The total tardiness  3
t

## Slide 5: State of the Art
Literature | Optimization Objective | Decomposition Strategies | Overlapping | Solution Approach | Compressing Time Window
Singer Marcos [2001] | Tardiness | Rolling Horizon (single machine) |  | Shifting Bottleneck | —
Liu et al. [2008] | Tardiness | Prediction Model | — | Genetic Algorithm | —
Zhang Rui, and Cheng Wu [2010] | Tardiness | Bottleneck Machine (dynamically) | — | Simulated Annealing Genetic Algorithm | —
Zhai et al. [2014] | Tardiness | Bottleneck Machine | — | Dispatching Rules Genetic Algorithm | —
Proposed | Makespan | Job/Machine Based |  | Logic Programming (Answer Set Programming) | 

## Slide 6: JSP Graph with 4 Jobs and 3 Machines
3,2
*
1,3
1,2
3,1
2,1
1,1
3,3
2,3
2,2
0
3
Conjunctive arc:
Disjunctive arc:
4,1
4,2
4,3

## Slide 7: Decomposition for JSP
3,2
*
1,3
1,2
3,1
2,1
1,1
3,3
2,3
2,2
0
Conjunctive arc:
Disjunctive arc:
4,1
4,2
4,3

## Slide 8: Decomposition for JSP cont’
O 3,1
O 4,3
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
O 1,1
O 1,2
O 3,3
O 2,3
O 1,3
O 5,1
O 5,2
O 5,3
O 6,1
O 6,2
O 6,3
O 7,2
O 7,3
O 7,1
Time Window 1
Time Window 2
Time Window 3

## Slide 9: Decomposition for JSP cont’
O 3,1
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
Time Window 1
First Iteration

## Slide 10: Decomposition for JSP cont’
O 3,1
O 4,3
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
O 1,1
O 1,2
O 3,3
O 2,3
O 5,1
O 6,1
O 7,1
Time Window 1
Time Window 2
Second Iteration

## Slide 11: Decomposition for JSP cont’
O 3,1
O 4,3
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
O 1,1
O 1,2
O 3,3
O 2,3
O 1,3
O 5,1
O 5,2
O 5,3
O 6,1
O 6,2
O 6,3
O 7,2
O 7,3
O 7,1
Time Window 1
Time Window 2
Time Window 3
Third Iteration

## Slide 12: Decomposition Strategies
 | Job | Machine
Earliest Starting Time (EST) | J-EST | M-EST
Most Total Work Remaining (MTWR) | J-MTWR | M-MTWR
Operation Ordering Criteria

## Slide 13: J-EST Decomposition
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
EST
0
4
7
10
12
9

## Slide 14: J-EST Decomposition cont’
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
EST
0
4
7
10
12
9

## Slide 15: J-EST Decomposition cont’
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
EST
0
4
7
10
12
9

## Slide 16: J-EST Decomposition cont’
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
EST
0
4
7
10
12
9

## Slide 17: J-EST Decomposition cont’
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
EST
0
4
7
10
12
9

## Slide 18: J-EST Decomposition using ASP
numofoperations(M1) :- M1 = NumofJobs * NumofMachs, numofJobs(NumofJobs), numofMachines(NumofMachs).
numOfOperPerTWin(M2) :- numOfOperations(M1), M2 = (M1 + numOfTimeWindows - 1) / numOfTimeWindows.
estimateStartTime(JobNum, 1, 0) :- operation(JobNum, 1).
estimateStartTime(JobNum, StepNum + 1, StartTime + ProTime) :- estimateStartTime(JobNum, StepNum, StartTime), proTime(JobNum, StepNum, ProTime), operation(JobNum, StepNum + 1).

## Slide 19: J-EST Decomposition using ASP cont’
index(JobNum, StepNum, N) :- estimateStartTime(JobNum, StepNum, StartTime),
proTime(JobNum, StepNum, ProTime),
N = #count{JobNum1, StepNum1 :
estimateStartTime(JobNum1, StepNum1, StartTime1),
proTime(JobNum1, StepNum1, ProTime1),
(StartTime1, ProTime1, StepNum1, JobNum1) <
(StartTime , ProTime , StepNum , JobNum) }.
assignToTimeWindow(JobNum, StepNum, (N + M) / M) :- index(JobNum, StepNum, N), numOfOperPerTWin(M).

## Slide 20: Machine Sequencing using ASP cont’
seqM((JobNum1, StepNum1), (JobNum2, StepNum2), ProTime1) :-
sameMach(JobNum1, StepNum1, JobNum2, StepNum2), proTime(JobNum1, StepNum1, ProTime1), assignToTimeWindow(JobNum1, StepNum1, t - 1), assignToTimeWindow(JobNum2, StepNum2, t).
{seqM((JobNum1, StepNum1), (JobNum2, StepNum2), ProTime1)} :-
sameMach(JobNum1, StepNum1, JobNum2, StepNum2), proTime(JobNum1, StepNum1, ProTime1), assignToTimeWindow(JobNum1, StepNum1, t), assignToTimeWindow(JobNum2, StepNum2, t).
seqM((JobNum2, StepNum2), (JobNum1, StepNum1), ProTime2) :-
sameMach(JobNum1, StepNum1, JobNum2, StepNum2), proTime(JobNum2, StepNum2, ProTime2), assignToTimeWindow(JobNum1, StepNum1, t), assignToTimeWindow(JobNum2, StepNum2, t), not seqM((JobNum1, StepNum1), (JobNum2, StepNum2), ProTime1).

## Slide 21: M-EST Decomposition
Machine 3
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
Machine 1
Machine load
10
20
11
Machine 2

## Slide 22: M-EST Decomposition cont’
Machine 3
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
Machine 1
Machine load
10
20
11
Machine 2

## Slide 23: M-EST Decomposition cont’
Machine 3
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
Machine 1
Machine load
10
11
11
Machine 2

## Slide 24: M-EST Decomposition cont’
Machine 3
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
Machine 1
Machine load
10
11
11
Machine 2

## Slide 25: M-EST Decomposition cont’
Machine 3
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
Machine 1
Machine load
6
5
11
Machine 2

## Slide 26: M-EST Decomposition cont’
Machine 3
O 3,1
O 2,1
O 2,2
O 3,2
O 1,1
O 1,2
O 3,3
O 1,3
10
O 2,3
4
9
0
0
12
4
7
0
Machine 1
Machine load
0
0
0
Machine 2

## Slide 27: Job- and Machine-based Decomposition
Size | 50  15 |  | 50  20 |  | 100  20 | 
Strategy | Makespan | Time | Makespan | Time | Makespan | Time
J – EST | 3524.8 | 1000.0 | 3540.8 | 1000.0 | 6964.4 | 1000.0
J – MTWR | 3456.2 | 1000.0 | 3561.0 | 1000.0 | 7149.6 | 1000.0
M – EST | 3083.8 | 1000.0 | 3260.3 | 944.9 | 6031.9 | 1000.0
M – MTWR | 3060.3 | 1000.0 | 3287.9 | 986.1 | 5948.6 | 1000.0
M – EST d | 3098.4 | 1000.0 | 3309.5 | 1000.0 | 6115.1 | 1000.0
M – MTWR d | 3041.6 | 1000.0 | 3287.0 | 980.4 | 6167.3 | 1000.0

## Slide 28: Overlapping

## Slide 29: Overlapping Time Windows
O 3,1
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
Time Window 1
First Iteration

## Slide 30: Overlapping Time Windows cont’
O 3,1
O 4,3
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
O 1,1
O 1,2
O 3,3
O 2,3
O 5,1
O 6,1
O 7,1
Time Window 1
Time Window 2

## Slide 31: Overlapping Time Windows cont’
O 3,1
O 4,3
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
O 1,1
O 1,2
O 3,3
O 2,3
O 5,1
O 6,1
O 7,1
Time Window 1
Time Window 2
Second Iteration
Overlapping

## Slide 32: Overlapping Time Windows cont’
O 3,1
O 4,3
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
O 1,1
O 1,2
O 3,3
O 2,3
O 5,1
O 6,1
O 7,1
Time Window 1
Time Window 2
Second Iteration

## Slide 33: Overlapping Time Windows cont’
O 3,1
O 4,3
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
O 1,1
O 1,2
O 3,3
O 2,3
O 5,1
O 6,1
O 7,1
Time Window 1
Time Window 2
Second Iteration
O 1,3
O 5,2
O 5,3
O 6,2
O 6,3
O 7,2
O 7,3
Time Window 3

## Slide 34: Overlapping Time Windows cont’
O 3,1
O 4,3
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
O 1,1
O 1,2
O 3,3
O 2,3
O 5,1
O 6,1
O 7,1
Time Window 1
Time Window 2
Second Iteration
O 1,3
O 5,2
O 5,3
O 6,2
O 6,3
O 7,2
O 7,3
Time Window 3
Overlapping

## Slide 35: Overlapping Time Windows cont’
O 3,1
O 4,3
O 2,1
O 2,2
Machine 3
Machine 2
Machine 1
O 4,1
O 4,2
O 3,2
O 1,1
O 1,2
O 3,3
O 2,3
O 5,1
O 6,1
O 7,1
Time Window 1
Time Window 2
Third Iteration
O 1,3
O 5,2
O 5,3
O 6,2
O 6,3
O 7,2
O 7,3
Time Window 3

## Slide 36: Overlapping Time Windows using ASP
index(JobNum1, StepNum1, N) :- startTime((JobNum1, StepNum1), StartTime1),
proTime(JobNum1, StepNum1, ProTime1),
assignToTimeWindow(JobNum1, StepNum1, t-1),
N = #count{JobNum2, StepNum2 :
startTime((JobNum2, StepNum2), StartTime2),
proTime(JobNum2, StepNum2, ProTime2),
assignToTimeWindow(JobNum2, StepNum2, t-1),
(StartTime1, ProTime1, StepNum1, JobNum1) <
(StartTime2, ProTime2, StepNum2, JobNum2) }.
overlappedOperation(JobNum, StepNum, t) :- index(JobNum, StepNum, N), numOfOperPerTWin(M),
assignToTimeWindow(JobNum, StepNum, t-1),
N < (3 * M / 10).

## Slide 37: Machine Sequencing with Overlapping
{seqM((JobNum1, StepNum1), (JobNum2, StepNum2), ProTime1)} :-
sameMach(JobNum1, StepNum1, JobNum2, StepNum2), proTime(JobNum1, StepNum1, ProTime1), overlappedOperation (JobNum1, StepNum1, t), assignToTimeWindow(JobNum2, StepNum2, t).
seqM((JobNum2, StepNum2), (JobNum1, StepNum1), ProTime2) :-
sameMach(JobNum1, StepNum1, JobNum2, StepNum2), proTime(JobNum2, StepNum2, ProTime2), overlappedOperation(JobNum1, StepNum1, t), assignToTimeWindow(JobNum2, StepNum2, t), not seqM((JobNum1, StepNum1), (JobNum2, StepNum2), ProTime1).
&diff{ Operation1 - Operation2 } <= -ProTime1 :- seqM(Operation1, Operation2, ProTime1), Operation2 = (JobNum2, StepNum2), assignToTimeWindow(JobNum2, StepNum2, t).

## Slide 38: Freezing Non-Overlapped Operations
&diff{ 0 – (JobNum, StepNum) } <= - StartTime :-
startTime((JobNum, StepNum), StartTime), assignToTimeWindow(JobNum, StepNum, t-1), not overlappedOperation(JobNum, StepNum, t).
&diff{ (JobNum, StepNum) – 0 } <= StartTime :-
startTime((JobNum, StepNum), StartTime), assignToTimeWindow(JobNum, StepNum, t-1), not overlappedOperation(JobNum, StepNum, t).

## Slide 39: Compression

## Slide 40: Optimized Time-window
Machine 3
Machine 2
Machine 1
O 3,2
O 1,1
O 1,2
O 2,3
O 1,3
O 2,2
O 2,1
O 3,1
O 3,3
Operation | Starting time | PT
O 1,1 | 0 | 9
O 1,2 | 9 | 3
O 1,3 | 12 | 5
O 2,1 | 0 | 4
O 2,2 | 9 | 6
O 2,3 | 17 | 2
O 3,1 | 0 | 4
O 3,2 | 12 | 3
O 3,3 | 15 | 5
20

## Slide 41: Compression Process
Machine 3
Machine 2
20
Machine 1
O 3,2
O 1,1
O 1,2
O 2,3
O 1,3
O 2,2
O 2,1
O 3,1
O 3,3
2nd
3th
1st
4th
5th
7th
8th
6th
9th
4
12
7

## Slide 42: Compression Process
O 1,1
O 2,1
O 3,1
O 1,2
O 2,2
O 1,3
O 3,2
O 3,3
O 2,3
O 3,2
20
Machine 3
Machine 2
Machine 1
4
12
7

## Slide 43: Overlapping Ratio
Size | 50  15 |  | 50  20 |  | 100  20 | 
Overlap | Makespan | Time | Makespan | Time | Makespan | Time
0 % | 3083.8 | 1000.0 | 3260.3 | 944.9 | 6031.9 | 1000.0
10 % | 3050.0 | 1000.0 | 3194.9 | 1000.0 | 5979.9 | 1000.0
20 % | 3046.0 | 1000.0 | 3200.6 | 1000.0 | 5954.3 | 1000.0
30 % | 3051.2 | 1000.0 | 3451.8 | 1000.0 | 6933.3 | 1000.0
Compression |  |  |  |  |  | 
0 % | 3010.3 | 907.5 | 3174.5 | 839.6 | 5671.9 | 1000.0
10 % | 2960.6 | 989.4 | 3154.6 | 956.4 | 5637.5 | 1000.0
20 % | 2946.9 | 1000.0 | 3120.3 | 1000.0 | 5640.7 | 1000.0
30 % | 2932.9 | 1000.0 | 3169.0 | 1000.0 | 5722.7 | 1000.0

## Slide 44: ASP vs OR-tools
 |  | OR – tools |  | Multi – shot |  | Single – shot | 
Size | Optima | Makespan | Distance | Makespan | Distance | Makespan | Distance
50 15 | 2773.8 | 2778.8 | 5.0 | 2932.9 | 159.1 | 3542.1 | 768.3
50 20 | 2843.9 | 2914.3 | 70.4 | 3120.3 | 276.4 | 3879.4 | 1035.5
100 20 | 5365.7 | 5559.3 | 193.6 | 5637.5 | 271.8 | 46786.1 | 41420.4

## Slide 45: Conclusions
We developed four different decomposition strategies for JSP
Bottleneck machines are essential during the decomposition process
Overlapping between time windows is effective in improving the solution quality
Post-processing phase (compression) prevented obtaining bad results and improved the model performance
Machine Learning approaches can improve the decomposition results (recently published results at PADL 2022)
Application in industrial scenarios is ongoing